## Slide 1
Know about personal protective equipment used in a logistic environment

## Slide 2
Outline how different types of personal protective equipment protect from injury/harm in a logistic environment (2.1)
Learning outcomes

## Slide 3
Personal Protective Equipment (PPE)
Outline how different types of personal protective equipment protect from injury/harm in a logistic environment

## Slide 4: Personal Protective Equipment PPE
Why is PPE important?
Discuss.
Can you name 10 examples of PPE a lorry driver might use?
Do you know what to do if your PPE becomes unusable?
Who has a duty to provide an employee with PPE?

## Slide 5
Employer vs Employee Responsibility?
It is the responsibility of your employer
to issue you with the correct PPE, in a fit, safe and
serviceable condition.
At the time of issue you should be
shown/ instructed on how to use it correctly.
It is your responsibility to ensure that your
PPE is safe to use and that you wear the correct
PPE at all times.
Personal Protective Equipment PPE

## Slide 6
Safety glasses can withstand low energy impacts of up to 45m per second
I want you to convert this into MPH = ​
Answer:
100.66MPH

## Slide 7
I want you to convert this into MPH = ​
Answer:
268.43MPH
Safety goggles can withstand medium impacts of up to 120m per second.
These protect you against - liquid splashes, gas, fine particles, molten metals and hot solids.

## Slide 8
Face shields protect against high energy impacts of up to 190m per second Liquid droplets, molten metals and hot solids.
I want you to convert this into MPH = ​
Answer:
425.01MPH

## Slide 9: FFP1 reduces exposure by a factor of four. Provides protection against large dust particles, which gives basic protection for situations such as sweeping dusty areas or cutting wood.
Mask

## Slide 10: FFP2 reduces exposure by a factor of ten. It provides protection against lung damaging dusts from sanding and grinding.
Mask

## Slide 11: FFP3 reduces exposure by a factor of twenty. It protects against highly toxic and damaging materials such as Asbestos, bacteria and metal dust.
Mask

## Slide 12: What to look for when purchasing a pair of safety boots?
Safety Boots

## Slide 13
Safety helmets
Safety helmets should be looked after.
They should not be used past their expiry date
They should be disposed of if dropped from height
Stickers or paints should not be applied to the shell as they can weaken the plastic.
Safety helmets should be looked after in a number of ways. They have an expiry date on, that has to be adhered to. If a helmet is dropped from height it should be scrapped and stickers or paints should not be applied to the shell as they can weaken the plastic.

## Slide 14: Safety helmets are made of thermoplastics and protect the head by spreading impacts evenly over the head through a simple shock absorption system.
Safety helmets

## Slide 15: Give basic protection against various materials.
Rigger gloves

## Slide 16: More protection and better dexterity.
PVC dotted nylon gloves

## Slide 17: Latex coated palm and fingers gives a superior grip for manual handling.
Gripper gloves

## Slide 18: Made from a mixture of Kevlar, Steel, Nylon and Glass Fibre to give a high level of protection with good dexterity. Used for handling glass, metal, concrete blocks and lumber.
Cut resistant gloves

## Slide 19
Quiz
Now test your knowledge with a quick Kahoot quiz

## Slide 20
Q4. Outline how different types of personal protective equipment protect from injury/harm in a logistic environment (2.1)
Complete workbook: Working Safely in Logistics

## Slide 21
Next Session
Know about health and safety practices and procedures in a logistics environment